## Slide 1: Introduction to exercise/discussion on aquatic risk assessment
Brasilia March 2016
Lilian Törnqvist

## Slide 2: 1. Use an example product and the EFSA conclusion report
Product | Super plus
Active substance | Methomyl
Concentration of active substance | 200 g/L
Intended use | Tomatoes
Application rate | 400 g a.s./ha
Number of applications | 2
Interval between applications | 14 days
Application method | Sprayer

## Slide 3: Find acute toxicology to earthworms
Check EFSA conclusion report at point ”Effects on earth worms (Annex IIA points 8.4 and 8.5) in the ”end point list”

## Slide 4: 2. Find acute toxicity to earthworms

## Slide 5: Find acute toxicity to aquatic organisms
Check EFSA conclusion report at point ”toxicity data for aquatic species (most sensitive species for each group) Annex IIA point 8.2 Annex IIIA point 10.2) in the “end point list”.

## Slide 6: 2. Find acute toxicity aquatic organisms

## Slide 7: Calculate PEC (soil)

## Slide 8: Calculate PEC (surface water)

## Slide 9: Predicted Environmental Concentation (PEC)
Organism | Acute toxicity | PEC
Earthworm | 0.19 mg/kg | 0.84 mg/kg
Fish | 630 µg/L (0.63 mg/L) | 10.47 µg/L
Algae | 17 µg/L (0.017 mg/L) | 10.47 µg/L
Aquatic invertebrates | >100 000 µg/L >100 mg/L | 10.47 µg/L

## Slide 10: Table of toxicity data
Organism | Acute toxicity
Earthworm | 0.19 mg/kg
Fish | 630 µg/L (0.63 mg/L)
Algae | 17 µg/L (0.017 mg/L)
Aquatic invertebrates | >100 000 µg/L >100 mg/L

## Slide 11: Risk assessment (EU Plant Protection Products)
Organism | Acute toxicity | PEC | TER
Earthworm | 0.19 mg/kg | 0.84 mg/kg | 0.23
Fish | 630 µg/L (0.63 mg/L) | 10.47 µg/L | 5,86
Aquatic invertebrates | 17 µg/L (0.017 mg/L) | 10.47 µg/L | 1.63
Algae | >100 000 µg/L >100 mg/L | 10.47 µg/L | >9 551
TER < Trigger = RISK
TER trigger
10
100
100
10
Risk
Yes
Yes
Yes
No