## Slide 1
Pesticide management including comparative assessment
Lilian Törnqvist, March 2016

## Slide 2: Content
FAO: Code of conduct
Criteria: FAO: Highly Hazardous Pesticides
Pesticides regulation today
Decisions
Share of work burden in EU
Discussion

## Slide 3: FAO: Code of conduct on pesticide management

## Slide 4: European Union: Common decision –making criteria at product level based on risk assessments “Uniform Principles” Annex VI
General Principles
Specific Principles
  Human health:
    Consumers: ADI (Acceptable Daily Intake), ARfD,(Acceptable reference Dose)
    Operators, bystander, workers: AOEL (Acceptable Operator Effect Level)

## Slide 5: Decision –making criteria product level based on risk assessments “Uniform Principles” Annex VI
  No authorisation should be granted if:
  Persistence: DT50> 3 months; DT90>1 year
  Groundwater or surface water used for extraction of drinking water: 0,1 µg/l or 1/10 of the ADI (if lower)
  BCF>1000 for readily degradable or >100 for not readily degradable
  Unless it is scientifically demonstrated that under field conditions…..

## Slide 6: Decision –making criteria product level based on risk assessments “Uniform Principles” Annex VI
Impact on non-target species, no authorisation if TER:
Birds/mammals: < 10 acute; <5 long- term; BCF>1 in fat tissue
Fish/Daphnia: < 100 acute; < 10 long-term
Algae: < 10 acute
Earthworms: short-term < 10; long-term < 5
Beneficial arthropods:>30% affected
Bees: Hazard quotient >50
  Unless it is scientifically demonstrated that under field conditions…..

## Slide 7: Plant protection Products in EU
New regulation on PPP: Regulation 1107/2009; Applicable 14 June 2011
  New cut off criteria: CMR category 1A and 1B, endocrine disrupters and very persistent and bio-accumulating substances not to be approved (↔”serious danger to plant health”, 5 years extra, but not canc. or repro. cat 1A)
  Substitution by comparative assessment of products
  Zonal authorization
  Safeners and synegists to be approved according to the same procedure as for active substances.
    A work plan established by 14 December 2014.
  Co-formulants: Negative list Annex III
  Uniform Principles for authorisation of products the same as before.

## Slide 8: Use of comparative assessment and decision-making criteria
Withdrawal due to policy criteria
Withdrawal or phasing out due to hazard / risk assessment
Aim for the future
Level of concern
Comparative risk assessment and risk benefit analysis on product level
Simplified procedures
e.g. WHO class 1a or b acute toxic substances; or GHS classes Carcinogenic, Mutagenic substances and substances toxic to Reproduction (Cat 1a and b)
Notes: This is an attempt to show the approach used to facilitate and speed up the decision-making during the extensive review. A set of principals and criteria were set up at the substance level to identify unacceptable pesticides. Comparative risk assessments were predominantly conducted at the product level.

## Slide 9: Substitution criteria
an existing product or non-chemical method is significantly safer for human/animal health or the environment; and
It presents no significant economic or practical disadvantages; and
the chemical diversity is adequate to minimize the occurrence of resistance.
Substitution is only possible if
Notes: Although they were worded in another way, these were also the criteria used in Sweden. In the PPP regulation there is a fourth criteria saying “Consequences for minor uses are taken into account”. However, it doesn’t seem to add anything, since it is already covered in point 2 and 3.

## Slide 10: Substitution example A chemical versus a non-chemical method
Chemical methods | Non-chemical control and prevention methods
Post harvest disease control on fruit and ware table potatoes | Climatic control of storage diseases. ULO (Ultra Low Oxygen) and low temperature in warehouses.
Soil disinfection | Preventive methods such as crop rotation, use of resistant crop varieties and to avoid cultivation of susceptible crops in infected areas.
Aquatic weed control | Mechanical weed control and dredging in ditches and watercourses.
Examples:
Notes: Example 3
Several actions, mandatory and voluntary have promoted the shifting from chemical to non-chemical control methods in these cases.
Not very common. The few existing cases have not been applied in a regular manner (according to the tiered approach).
It can sometimes lead to very complex assessment if, for instance the environmental impact due to the energy consumption and energy quality is also taken into account.
Covered by Article 50.1 and 50.2
These examples fulfil the requirement of being in general use (for more than 20 years).

## Slide 11: Substitution example product level
formulation | Formulation causing less risks
Powder | Suspension /liquid Wax block
Toxic solvent | Solvent less toxic
Need to mix with water/solvent | Ready to use /soluble small package
Etc. | 
Notes: Example 3
Several actions, mandatory and voluntary have promoted the shifting from chemical to non-chemical control methods in these cases.
Not very common. The few existing cases have not been applied in a regular manner (according to the tiered approach).
It can sometimes lead to very complex assessment if, for instance the environmental impact due to the energy consumption and energy quality is also taken into account.
Covered by Article 50.1 and 50.2
These examples fulfil the requirement of being in general use (for more than 20 years).

## Slide 12: ”User classification” of products
Besides the ”ordinary” EU classification and labelling pesticide products, Sweden has a special “user” classification, which are put in one of three user groups, to define needs of training. - Class 3 products can be used by anyone, no need for education (low hazard / risk) - Class 2 – only for users who have training - Class 1 additional training and a permit is required