## Slide 1: Environmental Exposure and Risk Assessment
Lilian Törnqvist
Brasilia, March 2016

## Slide 2: Topics
Why do an environmental risk assessment?
Which parts of the environment?
What tools do we have to estimate the exposure?
What tools do we have to estimate the risk?

## Slide 3: Risk Assessment
Tools for decision making based on predicted environmental effects
Hazard assessment – based on basic properties only (e.g. classification)
Estimation of environmental exposure
→ Possibility to do a risk assessment and to make some sort of decision (rejection, request for more data, approval, restrictions, etc.)

## Slide 4: Environmental exposure assessment
Estimation of the concentrations/doses which organisms in environmental compartments (aquatic, terrestrial, food) are, or may be exposed to.
Given as:
PEC – Predicted Environmental Concentration

## Slide 5: Administration of a chemical in the environment → different exposure routes
  Water / sediment
  Soil / pore water
  Air
  Via food chain

## Slide 6: Standard target organisms
    Water organisms
    Sediment organisms
    Soil organisms
    Wastewater treatment organisms
    Top predators, exposed via the food chain (secondary poisoning)

## Slide 7: Exposure Assessment - relevant compartments PPP
Surface water
Soil
Groundwater
Birds and mammals
Bees

## Slide 8: Exposure Assessment – birds and mammals Food chain
Calculation of Daily Dietary Dose (DDD)
Treated seeds
Insects
Crops

## Slide 9: Predicted Environmental Concentration
Surface water (PECsw)
Sediment (PECsediment)
Soil (PECsoil)
Groundwater (PECgw)
Food chain (PECoral)
Sewage Treatment Plant (PECSTP)
Marine water (PECmarine)

## Slide 10: Exposure models
Model calculations in FOCUS:
Groundwater, surface water, persistence in soil
FOCUS Home *MACRO in FOCUS
In English “Safe plant protection”

## Slide 11: PEC groundwater in EU
PECgw should not exceed 0.1 µg/l. - Is the same value for all substances, and for relevant metabolites (RM) i.e. that have a biological activity) This is a politically decided endpoint - this means that this value is not compared with ADI - WHO has set other values for individual substances, based on ADI
During monitoring of drinking water, the limit is set to: - 0.1 µg/L for a single active substance and RM - 0.5 µg/L when you have more than one substance or RM

## Slide 12: Transformation: Example degradation in soil, (one dose)
Chart: Actual PEC (mg/kg)
| 0 | 1 | 2 | 4 | 7 | 14 | 21 | 28 | 45 | 60 | 100
Actual PEC (mg/kg) | 0.66667 | 0.65521 | 0.64396 | 0.62202 | 0.59051 | 0.52306 | 0.46331 | 0.41038 | 0.30567 | 0.2357 | 0.11785
Dose 500 g a.s. /ha

## Slide 13: Exposure Assessment (pesticides) To estimate concentrations; Realistic worst case scenario
Surface water (mg/liter)
Soil (mg/kg dw)
30cm
depth
Dose (g/ha)
5cm depth
Soil density=1.5g/cm³
START SIMPLE!!!
Groundwater (ug/liter)
Concentration
in pore water
(calculated with soil-water partitioning coefficient)

## Slide 14: Environmental effects assessment: General principle
Estimate a concentration below which effects are not expected
Identify critical effects (e.g. reproduction, behaviour, immobilisation, growth)
Calculate dose – response endpoint (L(E)C50 or NOEC)
Add an Assessment/Safety Factor
100%
Response
Concentration
L(E)C50
50%
NOEC

## Slide 15: Standard organisms used for testing
Surface water: Algae, arthropods, fish
Soil: Earthworms, Micro-organisms

## Slide 16: Refinement – toxicity data
More realistic tests
field tests (mesocosm)
Laboratory tests with additional species of animals or plants

## Slide 17: Assessment/safety factor
Reflects the degree of uncertainty in extrapolation from laboratory toxicity test data for a limited number of species to the 'real' environment.
AF applied for long-term tests are lower than for short-term tests.
Why?  reduced uncertainty of extrapolation from laboratory data to the natural environment.
Therefore long-term data are preferred over short-term data.

## Slide 18: Safety/Assessment factors and PNEC: Industrial/ consumer chemicals and biocides
Predicted No Effect Concentration (PNEC)
is calculated from NOEC or ECx
divided by an assessment factor
Example PNECsurface water
Available data | Assessment Factor
At least one short-term LC50 from each of 3 trophic levels (base dataset) | 1000
One long-term NOEC | 100
Two long-term NOECs from different trophic levels | 50
Long term NOECs from at least 3 species in three different trophic levels | 10

## Slide 19: Safety factors - plant protection products
TER (Toxicity Exposure Ratio) values are ”political values”, agreed in Regulation EU1107/2011, not scientifically based
Examples:
Acute toxicity to aquatic organisms: TER 100
Acute toxicity to earthworm: TER 10
Long-term toxicity to birds: TER 5

## Slide 20: Risk assessment - plant protection products
1. Compare estimated concentration in the environment with compartment effect concentations
is calculation of Toxicity Exposure Ratio (TER)
2. Compare with safety factor
Generally:
TER > safety factor  OK
TER < safety factor  RISK
LC50
RISK?
PECsw

## Slide 21: Substances of Very High Concern (SVHC)
Toxic
Persistent
Bioaccumulating

## Slide 22
Producers
Primary consumers
Secondary consumers
A few species from different levels in the food web representing the whole ecosystem

## Slide 23: Bioaccumulation
Time (days)
Cfish
BCF= Cfish/Cwater at steady state (OECD GD 305: Bioconcentration: Flow-through Fish Test)
Cwater
Cwater
Cwater
Cwater
- Assessed with the Bioconcentration factor (BCF)
The net result of uptake, transformation and elimination of a substance in an organism

## Slide 24: Substances of high concern
PBT - Persistent, Bioaccumulating, and Toxic substances are substances of high concern
vP/vB - Very Persistent and very Bioaccumulating substances have potential to build up in organisms Long-term effects (e.g. reduced fertility) can cause problems in the future
PBT/vPvB assessments are carried out to protect systems where risks are difficult to estimate, e.g. long range transport of persistent substances

## Slide 25: The PBT / vPvB criteria
Property | PBT-criteria | vPvB-criteria
Persistence* | T1/2 > 60 days in marine water, or | T1/2 > 60 days in marine, fresh- or estuarine water, or
 | T1/2 > 40 days in fresh- or estuarine water, or | T1/2 > 180 days in marine, fresh- or estuarine sediment, or
 | T1/2 > 180 days in marine sediment, or | T1/2 > 180 days in soil.
 | T1/2 > 120 days in fresh- or estuarine sediment, or | 
 | T1/2 > 120 days in soil. | 
* T1/2 is the half-life of the chemical in the specific environment
P

## Slide 26: The PBT / vPvB criteria
Property | PBT-criteria | vPvB-criteria
Bio-accumulation | BCF > 2000 L/kg | BCF > 5000 L/kg
Toxicity | NOEC < 0.01 mg/L for marine or freshwater organisms, or | 
 | substance is classified as carcinogenic (category 1 or 2), mutagenic (category 1 or 2), or toxic for reproduction (category 1, 2 or 3), or | 
 | there is other evidence of chronic toxicity | 
B and T

## Slide 27: Take home message:
Do a stepwise risk assessment!
Start simple! Realistic worst case scenario.
Use information that is already available!